## Slide 1
Intelligent Robots: Algorithms and Systems
(CS5478)
Reinforcement learning
for Pick-Nav-Reach Task
SAC and TD3 with hindsight experience replay
Lin Chieh and Elston
1 / 5
Notes: Suggested delivery: 20 seconds.
This project studies reinforcement learning for the Pick-Nav-Reach task. A wheeled robot arm must pick up a block, carry it through a maze, and place it at a target. I will compare SAC and TD3, both using hindsight experience replay.
SAC (Soft Actor-Critic) and TD3 (Twin Delayed Deep Deterministic Policy Gradient)
Project source: mobile_manipulation_project_guide.md.

## Slide 2
Task and objective
2 / 5
PyBullet simulation with state observations
Grasp and lift
Arm and gripper
Carry through maze
Mobile base
Place and release
Arm and gripper
Objective
Compare learning efficiency and full-task success
across algorithms and gripper configurations.
Notes: Suggested delivery: 55 seconds.
The environment is a PyBullet maze with a wheeled arm. The task has three stages: establish a physical grasp and lift the block, navigate while retaining it, then place and release it stably at the target. We use numerical simulator state rather than camera images. The research objective is to compare how efficiently two learning algorithms acquire this behaviour and how their complete-task performance changes with a gripper modification. The whole sequence must work in one uninterrupted episode.
Project source: mobile_manipulation_project_guide.md, core task and experimental protocol.

## Slide 3
Learning approach
3 / 5
Soft Actor-Critic (SAC)
Stochastic policy
Entropy regularization
Twin Delayed DDPG (TD3)
Deterministic policy
Delayed actor updates
Hindsight experience replay (HER)
Goal A, reached B
Replay with goal A
Replay with achieved goal B
Separate skill training with curricula
Fixed supervisor for complete-task execution
Notes: Suggested delivery: 80 seconds.
Both methods learn continuous actions from replayed experience. SAC learns a stochastic policy and includes an entropy term that encourages exploration. TD3 learns a deterministic policy and uses delayed actor updates, along with its other critic-stabilisation mechanisms. Both use HER. For example, an episode may aim for A but reach B. We retain experience with the original goal and also replay it with B as the goal, recomputing its rewards. This makes failed attempts more useful. Each of the three skills is trained with suitable starting states and curricula. A fixed supervisor switches between them, and low-level controllers translate commands into robot motion. The supervisor itself is not learned.
References:
Andrychowicz et al., Hindsight Experience Replay, NeurIPS 2017: https://arxiv.org/abs/1707.01495
SAC implementation: https://stable-baselines3.readthedocs.io/en/master/modules/sac.html
TD3 implementation: https://stable-baselines3.readthedocs.io/en/master/modules/td3.html
HER interface: https://stable-baselines3.readthedocs.io/en/master/modules/her.html

## Slide 4
Experimental design
4 / 5
Same wheeled base and arm
Robot configuration | SAC + HER | TD3 + HER
Original gripper | 3 seeds | 3 seeds
Modified gripper | 3 seeds | 3 seeds
12 independently trained systems
Matched task, training budgets and evaluation cases
Notes: Suggested delivery: 55 seconds.
The core experiment has four conditions: two learners on the original robot and on a modified gripper, keeping the same wheeled base and arm. The exact gripper modification will follow inspection of the supplied assets; a change in finger geometry or a coupled multi-finger gripper would be suitable. Each condition has three independent training seeds, giving twelve complete systems. A system includes all three trained skills. We match the task, assistance and total training-interaction budget, counting training across all skills. This compares algorithms using HER; it does not isolate the effect of HER itself.
Project source: mobile_manipulation_project_guide.md, learning algorithms and experimental protocol.

## Slide 5
Evaluation
5 / 5
Complete-task success
Lift, transport, release
and stable placement
Learning efficiency
Success versus total
training interactions
Failure analysis
Grasping, navigation,
drops and placement
Notes: Suggested delivery: 50 seconds.
The main measure is complete-task success from the real starting conditions. Success requires an actual lift and transport, followed by release and stable placement. We will also compare learning efficiency using success against total training interactions. A stage-level failure analysis will show whether differences come from grasping, navigation, drops or placement. Final tests use held-out starts and goals, with no resets between skills. We report results for each training seed as well as aggregate performance. The expected outputs are working trained controllers and a reproducible comparison of the four conditions.
Project source: mobile_manipulation_project_guide.md, experimental protocol and deliverables.

## Slide 6
Project Timeline
2 / 5
Period | Planned work | Completion milestone
Setup and feasibility | Validate the simulator, observations, actions, rewards and success criteria. Choose one specific gripper modification. Run short training pilots to estimate computing requirements. | A physically workable task, evaluation procedure and realistic training budget.
Skill training and integration | Develop grasping, navigation and placement policies with curricula. Connect them using explicit switching conditions in the fixed supervisor. Test handoffs between skills. | One working system that completes the entire task repeatedly.
Controlled experiments | Freeze settings and run SAC+HER and TD3+HER with both grippers and three seeds per condition. Evaluate using the same held-out starts and goals. | Completed experiments, saved models and evaluation logs.
Analysis and deliverables | Compare performance, investigate failures, prepare figures, and complete the report and demonstration. | Submission-ready results and demonstration.
Notes: Our schedule spans six to seven weeks.
Week one covers environment setup and feasibility checks. Weeks two and three focus on skill training and integration. Weeks four and five cover the controlled experiments. Week six is for analysis, the report, and the demonstration, with week seven reserved as a buffer.